## Slide 1: CHOPIN: Scalable Graphics Rendering in Multi-GPU Systems via Parallel Image Composition
Xiaowei Ren Mieszko Lis
The University of British Columbia

## Slide 2: Coming Up
Extend performance scaling of graphics rendering in the latest multi-GPUs
Prior bottlenecks: redundant computing and sequential inter-GPU communication
Our work:
Insight: eliminating prior bottlenecks by leveraging parallel image composition
Outperform the best prior scheme by up to 56% (25% gmean)

## Slide 3: Graphics Pipeline
Geometry
Processing
Rasterization
Fragment
Processing
Need multi-GPU solutions to meet increasing performance requirements
2D Screen Space
y
v
2
v
1
v
3
v
0
x
Fragments
Pixels
3D Object Space
v
2
v
1
v
3
v
0
Chas Boyd. The DirectX 11 Compute Shader. In SIGGRAPH 2008.

## Slide 4: Graphics Pipeline
v
2
v
1
v
0
3D Object
2D Screen
Fragments
Pixels
y
v
2
v
1
v
0
x
v
1
v
3
v
0
y
v
1
v
3
v
0
x
v
2
v
1
v
3
v
0
GPU 0
GPU 1
Inter-GPU synchronization is necessary for the final image generation
Inter-GPU synchronization cannot break the primitive depth order

## Slide 5: Bottleneck: Primitive Duplication
GPU2
GPU3
GPU0
GPU1
2D Screen
limited by inter-GPU links (e.g., SLI, CrossFire),
duplicate all primitives in each GPU
filter out primitives and fragments of other GPUs
simple, but limited by redundant computing
NVIDIA. SLI Best Practices. 2011.
assign screen regions to different GPUs
Modern inter-GPU links (e.g., NVLink, NVSwitch) enable
high-performance inter-GPU synchronization
2 8GPUs, % of Geo Process cycles 55%  75%

## Slide 6: Synchronization in Multi-GPU Rendering
G: Geometry Processing, R: Rasterization, F: Fragment Processing
Primitives
Display
R&F
R&F
G
G
Sync.
sort-first
Primitives
Display
R&F
R&F
Sync.
sort-middle
G
G
Primitives
Display
Sync.
sort-last
G
G
R&F
R&F
exchange raw-primitive
exchange screen-primitive
exchange fragments/pixels
Molnar et al. A Sorting Classification of Parallel Rendering. In CG&A 1994.
Large Traffic Load
CHOPIN

## Slide 7: Bottleneck: Sequential Inter-GPU Sync.
evenly distribute primitives to GPUs
requires sequential primitive distribution among GPUs
P: Projection D: Distribution G: Geometry Processing R: Rasterization F: Fragment Processing
Kim et al. GPUpd: A Fast and Scalable Multi-GPU Architecture using Cooperative Projection and Distribution. In Micro 2017.
GPUpd: a scheme of sort-first multi-GPU rendering
sequential inter-GPU communication becomes
critical bottleneck with more GPUs
G
G
G
G
R&F
R&F
R&F
R&F
D
D
D
D
P
P
P
P
GPU0
GPU1
GPU2
GPU3
2  8GPUs, % of stage D cycles 6%  29%

## Slide 8: Parallelism of Image Composition
Opaque Sub-image Composition:
Semi-transparent Sub-image Composition:

## Slide 9: Parallelism of Image Composition
Opaque Sub-image Composition: occlude pixels that are further to camera
A
B
C
GPU0
GPU1
GPU2
A
B
C
GPU0
GPU1
GPU2
A
B
C
GPU0
GPU1
GPU2
A
B
C
step 1
step 2
opaque sub-images can be composed out-of-order
C over B over A

## Slide 10: Parallelism of Image Composition
Bethel et al. High Performance Visualization: Enabling Extreme-Scale Scientific Insight (Chapter 5). In CRC Press 2012.
Semi-transparent Sub-image Composition: blending two pixels
A
B
C
GPU0
GPU1
GPU2
A
B
C
GPU0
GPU1
GPU2
A
B
C
GPU0
GPU1
GPU2
A
B
C
step 1
step 2
semi-transparent composition is not commutative, but it’s associative
start to compose adjacent sub-images once they are ready
C over B over A

## Slide 11: Parallelism of Image Composition
Opaque Sub-image Composition:
Semi-transparent Sub-image Composition:
Simply occlude pixels that are further to camera
can be composed out-of-order
blending two pixels, not commutative, but it’s associative
Start to compose adjacent sub-images once they are ready

## Slide 12: Leveraging Parallel Image Composition
Insight: sequential primitive distribution  parallel image composition
comp.
comp.
comp.
comp.
reduced
cycles
send draws to different GPUs, so
no redundant computing
compose sub-images in parallel
P: Projection D: Distribution G: Geometry Processing R: Rasterization F: Fragment Processing
G
G
G
G
R&F
R&F
R&F
R&F
D
D
D
D
P
P
P
P
GPU0
GPU1
GPU2
GPU3
GPUpd
G
G
G
G
R&F
R&F
R&F
R&F
GPU0
GPU1
GPU2
GPU3
CHOPIN

## Slide 13: Draw Command Scheduler
GPU0
GPU1
GPU2
GPU3
Draw0
Draw1
Draw2
Draw3
Draw4
Draw5
Draw6
Draw7
Distribute draw commands to GPUs with Round Robin scheduling
execution time of draw commands vary significantly
simple, but can create load imbalance very easily

## Slide 14: Draw Command Scheduler
Heuristic: more primitives waiting at geometry processing
indicates bigger remaining workload of the graphics pipeline
Geometry
Processing
Rasterization
Fragment
Processing
2D Screen Space
y
v
2
v
1
v
3
v
0
x
Fragments
Pixels
3D Object Space
v
2
v
1
v
3
v
0
Scheduler: schedule each draw to the GPU that has the smallest number
of remaining primitives in geometry processing
optimal load balancing requires ideal execution time estimation

## Slide 15: Image Composition Scheduler
Only start inter-GPU communication while
two GPUs are ready and available
GPU0
running
GPU1
done
GPU2
done
GPU3
done
congestion
scheduler table records GPU execution status
e.g., running? busy composing?

## Slide 16: Overall Performance
within 5% of the idealized system with image composition
0.0
0.4
0.8
1.2
1.6
GPUpd
Ideal-GPUpd
CHOPIN
Normalized Speedup
Ideal-CHOPIN
Duplication
25% faster than the best prior solution
8-GPU system, 8 real-world game traces

## Slide 17: Scaling to Modern and Future Games
Crysis Remastered (released in Sept. 2020)
average number of triangles: 12 million / frame
average primitive processing time: 11.57ms / frame
average fragment processing time: 11.11ms / frame
bigger number of triangles
longer primitive processing time
more redundant computing
larger sequential bottleneck
modern and future games favor schemes of parallel image composition

## Slide 18: Summary
Prior multi-GPU rendering mechanisms are not scalable due to redundant computing and sequential inter-GPU communication
Leveraging parallelism of image composition can eliminate the bottlenecks of prior work and extend performance scaling
Modern and future games favor schemes of parallel image composition

## Slide 19: Thank you
Contact me: xiaowei@ece.ubc.ca
This presentation and recording belong to the authors. No distribution is allowed without the authors' permission.